## Slide 1: Sphagnum farming as paludiculture on bogs for replacing peat in horticulture
Experiences in Northwestern Germany

## Slide 2: Contents
Introduction
Motivation
Area
Activities
Results
Foto: MoKuRa

## Slide 3: Introduction: the company
History
Founded around 1910 as agricultural enterprise
Peat extraction since1924
family owned since 1959
Today
350.000 cbm peat as raw material for growing media
80.000 cbm growing media for professional hort.
550 ha extraction area
ca. 1100 ha rewetted area
40 fte (full time employee equivalents)
3 apprentices
6 Mio Euro turnover per year
Certifications
ISO 9001:2015
RAL certification for growing media
RHP certifcation for peat
RPP Responsibly produced peat certification
Foto: MoKuRa

## Slide 4: Introduction: Paludiculture Projects
2004 - 2007
2010 – 2013
Moosfarm
2007 - 2010
2010 - 2014
SPHAKO 2015 – 2018
Production of Sphagnum based GM for professional horticulture
Trial Field Ramsloh:
on cut-over bog
Tests with Floating mats
Sphagnum Moss from Ramsloh, Finnland, Hankhausen
2011 - 2015
2011-2015
since
2015
Trial field Hankhausen:
on former bog grassland

## Slide 5
Mosaic of different Sphagnum farming types
on degraded bogs
Notes: neu

## Slide 6: Introduction: Project partners:
Carl-von-Ossietzky-University Oldenburg
Dr. Dittrich & Partner Hydroconsult GmbH Dresden
Ernst Moritz Arndt University Greifswald
Graalfs Horticulture Aurich
Humboldt University Berlin
IASP Berlin
Klasmann Deilmann, Groß-Hesepe
Agency for Soil, Mining and Geology of Lower Saxony, Bremen
LVG Ahlem
LVG Bad Zwischenahn, both Chamber of Agriculture of Lower Saxony
MST Drainage tools GmbH Twistringen
NIRA Groß Ippener
Rosengut Langerwisch
Textile Research Institute of Saxony, Chemnitz
Tree Nursery Scheper, Saterland
University Rostock
University of Applied Sciences Weihenstephan – Triesdorf
Notes: Emphasize a special one Klick

## Slide 7: Motivation
Insuring the future of the company because of difficulties in getting new extraction permits
Drive towards peat reduced potting mixes
Finding new land-use options for drained bog grasslands to reduce GHG emissions
Improving restoration techniques

## Slide 8: Area: Northwestern Germany
Data source: BÜK 500 000 © Federal Institute for Geosciences and Natural Resources Germany: Hannover 2014
Torfwerk Moorkultur Ramsloh Werner Koch GmbH & Co. KG
Test Field Hankhausen
©Nibis Kartenserver 2014 Bodenkarte LBEG Hannover
Notes: Hochmoorgebiete in Deutschland grün (Niedermoor olivgrün)

## Slide 9: Area: Lower Saxony
38 % of all peatlands in Germany are located in Lower Saxony
12% of all GHG emissions of Lower Saxony originate from drained peatlands (8% of land area)
ca 395.000 ha of peatlands and 135.000 ha of other organic soils
Notes: The agricultural part of the gross value in LS only 1,5%. Only 2,8% of all employees work in agriculture.

## Slide 10
Area: Current bog utilisation types in NW Germany
20.000 ha 92.000 ha 11.000ha
Notes: usage categories of drained raised bog areas: Grassland 92.000 ha, bush/heather/peatland 54.000 ha Acker auf Hochmoor (arable land) 20.000 ha forest 13.000 ha others (e.g. peat extraction 11.000ha ) 29.000ha based on Atkis basis DLM 2015 (niedersächsische Moorlandschaften) vgl. Natura 2000 50.800ha

## Slide 11: Activities: Enlarging the area
Ca. 1100 Squaremeter 13 Hectar
on cut-over bog on former bog grassland
Foto: MoKuRa
Foto: MoKuRa

## Slide 12: Activities: Spreading of Propagation material
Manually
with adepted machinery
Foto: MoKuRa
Foto: MoKuRa

## Slide 13: Activities: Water supply
Impoundment in ditches and drainage pipes with a small dam, water pump winddriven
Electric pumps with automatic regulation
Foto: MoKuRa
Foto: MoKuRa

## Slide 14: Activities: Management of vascular plants
String trimmer
Excavator with mowing masket
Foto: Uni Greifswald
Foto: Uni Greifswald
Notes: sling trimmer? brush cutter?

## Slide 15: Activities: Harvesting
Manually
Excavator with mowing basket
Foto: MoKuRa
Foto: MoKuRa

## Slide 16: Activities: Conditioning of Sphagnum for GM
Heat treatment
Screening
Foto: MoKuRa
Foto: MoKuRa
Foto: MoKuRa
Foto: MoKuRa

## Slide 17: Activities: Tests of GM with Sphagnum
Research Institution
Azalea, Gaultheria, Rhodendron
Malus, Pyracantha, Lonicera
Horticultural enterprises
Poinsettia
Vegetable seedlings
Calluna
Foto: MoKuRa
Foto: MoKuRa
Notes: Azalea, Checkerberry or wintergreen or eastern teaberry, Apples, Firethorn, box honeysuckle Winter rose, Heather or ling

## Slide 18
Mosaic of different Sphagnum farming types
on degraded bogs
2004-2014
Notes: neu

## Slide 19
mineral subsoil
black peat
white peat
ditch
irrigation pipe
Sphagnum lawn
inlet
outlet
N
20 m
5 m
a)
b)
cross section
piling
Gaudig et al. 2017
Size: ca. 60x20 m
Irrigation: pipes every 5 m and surrounding ditch
On black peat (H7), ca. 1.8 m thick
study site cut-over bog: schematic view

## Slide 20
November 2004
study site cut-over bog: spreading of mosses and straw
Foto: D. Kamermann
  Sphagnum papillosum
  fragment length 0.5-2 cm
  initial cover ~95% (brownish mosses)
Notes: 20

## Slide 21
Nov 2004
study site cut-over bog: after installation
Foto: D. Kamermann

## Slide 22
Continuous increase of vital (green) Sphagnum papillosum cover
Established after 45 months (3.75 years)
establishment
growth
Sphagnum papillosum cover
Gaudig et al. 2017
1
2
3
4
5
6
7
8
9
years after installation

## Slide 23
Continuous growth of Sphagnum papillosum lawn
Up to 19 cm (mean) after 10 years
Stagnation period = dry conditions
cm
Gaudig et al. 2017
1
2
3
4
5
6
7
8
9
years after installation
0
S. papillosum lawn thickness and water table

## Slide 24
Mosaic of different Sphagnum farming types
on degraded bogs
since 2010
Notes: neu

## Slide 25
April 2017
© Tobias Dahms/ Stephan Busse
study site bog grassland: 13 ha

## Slide 26
irrigation
ditch
Sphagnum lawn
causeway
inlet
outlet
aerial view
schematic view
Irrigation: ditches every10 m
On white peat (H3-6)

## Slide 27
June 2011
study site bog grassland: after installation
Foto: Uni Greifswald
Notes: Neues Bild

## Slide 28
study site bog grassland: ½ year after installation
Nov 2011
Foto: Uni Greifswald

## Slide 29
Foto: Uni Greifswald
study site bog grassland: 3 years after installation

## Slide 30
the success:
established lawn after 1.5 years
biomass productivity: ~8.7 t DM/ ha*yr
harvest possible after 3 years
© Uni Greifswald
Foto: Uni Greifswald

## Slide 31
Advantages of Sphagnum farming
  production of a renewable resource
  regional economic benefits
Foto: G. Block, MOKURA

## Slide 32
  reduction of GHG emissions: ~15 t CO2- eq. ha-1 yr-1
  stop of subsidence
Foto: Uni Greifswald
Günther et al. 2017
Advantages of Sphagnum farming
Notes: Plus Ersatz von fossilem Torf  ca 18 t

## Slide 33
  improvement of hydrology and regional climate
  decrease nutrient loads in surface waters: 64 kg N + 7 kg P ha-1 yr-1
Foto: Uni Greifswald
Temmink et al. 2017
Advantages of Sphagnum farming

## Slide 34
  habitats for endangered peatland species
Foto: Uni Greifswald
Muster et al. 2015
Advantages of Sphagnum farming

## Slide 35: Thanks for your attention!
Questions???